ARMS TECH LTD

5133 N. Central Avenue, Suite 200

### Phoenix, AZ, USA, 85012

### Tel. (602) 272-9045, Fax (602) 272-1922

# COMPACT POLICE CARBINE (CPC) Model 556

# Caliber 5.56mm NATO

(Fig. 1 AT LTD CPC-556 cal. 5.56mm NATO)

Officers being outgunned by heavily armed felons are being addressed by the authorization of shoulder arms.  In the case of motor officers, the problem has remained unaddressed.   The motorcycle officer is often the first lawman to appear at the scene of an incident and is nearly always equipped with just a handgun – and no backup.

To meet these requirement for an utterly reliable, lethal and durable semiautomatic carbine suitable for motor officers, AT LTD developed the Compact Police Carbine (CPC) Model 556.  Other than being capable of semiautomatic fire only, the CPC is identical to our full-automatic 5.56mm COMPAK-16.   Both designs feature a 24-inch overall length and a 9.5-inch, heavy profile 1:9 Rate-of-Twist (ROT) progressive gain-twist polygonal bore extended wear barrel, along with our patented gas trap operating system.  This gas management design provides a number of advantages, to include, improved controllability during sustained fire, easier maintenance, markedly superior barrel life, and vastly superior accuracy.  The very stiff polygonal 5.56mm barrel is made from a newly developed stainless steel designed specifically for sustained rapid and yet consistently accurate fire.  The result of our efforts is an extremely accurate and reliable weapon in a chambering suitable to the task at hand.  All this, in a package that easily fits into a locked Police Road King hard saddlebag – with room to spare.

(Fig. 2 CPC Gas Trap with Vortex Flash Eliminator and Flip-Up Front Sight.)

The 1:9 ROT provides excellent stability for all commonly encountered 5.56mm loadings available to law enforcement.  Unfortunately, issue M4s and their many copies largely come with the same 1:7 twist as the M16A2 and will not stabilize the 52 grain TAP round or any of the 55 grain rounds currently available.  The use of M855 62 grain military ball in law enforcement is questionable since this round was designed as armor piercing.  With the slower 1:9 ROT, together with it’s progressive gain twist in a polygonal bore configuration, the CPC system promises an extremely long service life.

(Fig. 3 AT LTD Compact Police Carbine - CPC in HD Road King Police Hard Bags)

SUPPRESSOR CAPABLE DESIGN.  Borrowing on lessons learned by our design team in developing our numerous suppressors currently in use with military special operations units, we have very recently developed our extremely robust and compact quick-disconnecting QD-223 suppressor, which is optimized for 5.56mm weapons systems.  This suppressor is fully compatible with the AT CPC. Further, the QD-223 suppressor does not detract from systems accuracy in the least.  The Smith Enterprise G-6A1 Vortex flash hider is an integral component of the QD-223 suppressor system and standard on the AT CPC.

(Fig.4 Optional AT LTD QD-223 Suppressor)

THE ECONOMIC ADVANTAGE.  Organizations needing a compact semiautomatic 5.56mm weapon can either purchase complete a complete CPC Model 556 system or take the very cost-effective route of simply upgrading their existing AR/M-16-type weapons to the CPC configuration by merely retrofitting our complete barreled upper receivers with matched bolt assemblies. Contact Arms Tech LTD for details on these programs.

(Revised 01 June 2004)