ARMS TECH LTD

5133 N. Central Avenue, Suite 200

### Phoenix, AZ, USA, 85012

### Tel. (602) 272-9045, STU-III (602) 275-9230, Fax (602) 272-1922

Federal Systems Division (727) 593-7342

#### Minimore-1 (MM-1) Miniature Field Loadable Claymore Mine

While the five-pound M18A1 has continues to serve admirably as a defensive system, it has evolved little since its first fielding in 1960.  In response to a Special Operations requirement for a flexible, lighter and more compact version of this weapon, Arms Tech LTD developed a version that is also quite unique in that it can be “loaded” in the field.  The operational and logistical considerations of the MM-1 design are as considerable as they are obvious.

In a SOF application operators can now fill the device once they have entered into the operational area.  Further, the MM-1 can be charged with a variety of available commercial or military-grade high explosive or even field expedient explosive.  For the explosive ordnance-trained specialist, the MM-1 opens up the possibility for highly flexible applications as well as use in logistically austere environments. For the logistician, the fact that the Minimore-1 is totally inert as delivered from our factory means that no safety considerations need apply during shipment or while in storage.

In tactical use, the MM-1 has another advantage over conventional directional anti-personnel mine designs. The MM-1 occupies only one-third the volume by area of a typical M-18A1. An operator can carry three MM-1s in place of one M-18A1.  This affords the operator the ability to carefully emplace multiple MM-1s using Economy of Force, complex “Kill Zones” are easily constructed.  In sum – synergy as applied to anti-personnel mine warfare.

The MM-1 can employ the same accessories associated with the M18A1, to include the M40 Circuit Tester and the M57 Electrical Firing Device.  Likewise, the MM-1 can employ a #2 Electrical Blasting Cap.  The MM-1 is lethal to the same range as the M18 A1 when charged with C-4 explosive.  Range and lethality is a function of the type of explosive fill employed.

General Specifications

Weight, 14.25 oz. unloaded

Height, 3.2 in

Width, 5.2 in

Anti-personnel fill:  Approximately 500 .215 in./ 5.5 mm spheres in a bonded matrix

(Information current as of 24 June 2003)