ARMS TECH LTD

5133 N. Central Avenue, Suite 200

### Phoenix, AZ, USA, 85012

### Tel. (602) 272-9045, STU-III (602) 275-9230, Fax (602) 272-1922

### Federal Systems Division (727) 593-7342

###### TACTICAL TAKEDOWN RIFLE MODEL 50 (TTR-50), Cal. 0.50

FINALLY, A PRACTICAL HEAVY SNIPER RIFLE. The heavy caliber sniper rifle is nothing new.  Since before World War One, various armies have approached the idea of delivering accurate fire at ranges beyond the range of their standard sniper systems and general purpose machineguns (GPMG) with varying degrees of success.  One common failing in all previous attempts to build a heavy sniper rifle (HSR) has been the obvious weight and size penalty imposed by these weapons.  This transportability problem has limited the tactical utility of these weapons when deployed.  Most often, such weapons have been transported tactically in light wheeled vehicles and then transported by foot only for short distances.

(Arms Tech LTD TTR-50 with 27.0” Barrel and MD-50B Sound and Flash Suppressor)

ENTER THE TTR-50.  Realizing this need for a truly man-portable HSR, Arms Tech LTD developed the TTR-50 shown above. Employing the proven and combat-tested McMillan 0.50 caliber repeater action,  this extremely robust and well though out design offers a number of innovations, to include a full diameter bolt with horizontally arrayed lugs, which in turn offers a vastly superior Sako-style extractor system.  Further, this 4340-chrome moly receiver has been very carefully heat treated after all machining operations have been accomplished. The bolt, manufactured from 9310 steel, which is a carburized type material, lending itself well to case hardening.  The trigger mechanism is set at 3.5 pounds, with a Jewell-type trigger being optional.

What sets the TTR-50 apart from other systems built around the McMillan 0.50 caliber action is the quick disconnecting (QD) barrel system.  By the addition of this proven mechanism, the TTR-50 becomes a truly practical and man portable heavy sniper rifle.  This QD system, first pioneered on the earlier AT LTD TTR-700 medium sniper rifle, was the first such device to prove that zero can be effectively maintained after removal and reattachment of the barrel.  In designing the TTR-50, the developers have thus fielded a highly modular HSR that will allow a sniper team to infiltrate, conduct operations and exfiltrate/extract from the operational area with previously unheard of tactical agility and stealth.  Likewise, the applicability of TTR-50 for special operations, parachute and other light forces is not to be overlooked.

DESIGNED FOR SUPPRESSED APPLICATIONS.  One of the biggest liabilities of the HSR has traditionally been the unique visual and aural signature produced by these large caliber weapons.    During Operation Desert Storm this problem was first noticed by UK and US SOF operators to the extent that several critical engagements were compromised by the unique signature of HSR.  To meet this requirement, AT LTD has recently developed the extremely effective MD-50B sound and flash suppressor, which has been adopted in quantity by USSOCOM for use on the Barrett M82A1 rifle.  This very robust and proven design is now a standardized component of the TTR-50 heavy sniper rifle when supplied to military and other official customers.

EASE OF MAINTENANCE.   Just as is the case with the smaller TTR-700 from which the TTR-50 was largely derived, this new weapon is extremely easy to maintain by virtue of the QD barrel system.  Additionally, when the barrel eventually becomes unserviceable over time or when operational requirements mandate a longer or shorter barrel, this simple operation is performed as easily as routine preventive checks and maintenance, thus reducing down time to virtually nil.

GENERAL SPECIFICATIONS

Caliber – 0.50 caliber (12.7 x 99mm)

Length, overall, stock extended, w/o barrel, inches (in) 				30 3/8

Length, overall, buttstock removed, w/o barrel, in.					19 ½

Width, in.

- without bolt handle,						2 3/8

- with bolt handle, 							3 ¾

Height, magazine inserted, with Picatinny Rail interface, w/o optics, in.			8.0

Weight, empty, w/o barrel, w/o optics, w/o buttstock, w/magazine, pounds/ounces (lb/oz)

12/7

Weight, buttstock, lb/oz					3/12

Weight, 27” barrel, w/o muzzle device, lb/oz*					10.0

Action -- Modified McMillan

Magazine capacity, number of rounds                                                                                    6

Barrel -- 27”, 1:15 ROT, Schneider, fluted, muzzle threaded for MD-50B Suppressor*.

Stock – McMillan TAC-50, (no tool required), available with spacer system for adjustable LOP.

Muzzle device – Arms Tech LTD MD-50B Sound and Flash Suppressor is supplied with weapon for USG and FMS customers.

Materials –

- Receiver --  4340 Chrome moly 45-48 Rockwell C.

- Bolt – 9310 Steel

- Barrel – 416R stainless steel*.

*NOTE: other barrel configurations upon request.

AVAILABILITY.  As a Title I firearm, the TTR-50 is one of very few Arms Tech LTD products available to the general consumer. Official USG agencies and FMS customers should contact Mr. Richard Pimley, Federal Systems Manager, (727) 593-7342, pimleyr@yahoo.com for current availability and USG pricing.

ISO 9001 CERTIFICATION.  Arms Tech LTD is an ISO 9001-certified developer and manufacturer of armaments and related technologies supporting the special operations community (ISO Certification NZ056095).  ISO-9001 is the most demanding of the various ISO standards for developers and producers.    DOD has endorsed this system for all contractors since 06 June 1991.